#### NANPE-166

INDUSTRY NUMBERING COMMITTEE (INC) CONTRIBUTION

NANPE WORKSHOP

TITLE:  Release of the first digit of the CO Code (N) for use by a Zero or One (X)

# ISSUES:  INC 159: “D” Digit Release Study

DATE:  March 4, 2000

SOURCE:  David Bench

Nortel Networks

4010 E. Chapel Hill Nelson Hwy, Mail Stop D17/02/0F2

Research Triangle Park, NC 27709

Tel:  919 991-7362

Fax:  919 997-1026

Email: dbench@nortelnetworks.com

ABSTRACT:  This contribution provides input on release of the first digit of the Central Office Code (N) portion of the NANP for use by a zero or one (X).  This contribution covers existing published uses of a “0” of “1” as the first digit.

NOTICE:

This contribution has been prepared by Nortel Networks to assist the INC NANPE Workshop.  This document is offered to the NANPE Workshop as a basis for discussion and is not a binding proposal on Nortel Networks.

NANP NETWORK (AT&T / BOC-LEC / Stentor-Canada / C&W-Caribbean / etc.)

ROUTING CODES  0XX / 1XX / special NXX

Includes historical use of some codes as well as many current generic uses

### Code - Description

000 - Rate Quote System

001 -> 005 - (spare- available for: TTC's, pseudo c.o. codes, etc.)

006 - Intl. ATME (TAS-2 Domain ONLY) 006 ->

008 - InWATS OSO routings (from multiple states/NPA's) (1960's/70's)

009 - Rate Quote System

010 - (RESERVED)

011 - IDDD Access / IOTC: International Originating Toll Center

012 - Alt.Route via Principal Tandem (i.e., due to Sector Tandem failure)

013 - (TWX function - but what?)

014 - 4-Row TWX Assistance Opr (954-1212 converts to 014-1212): from 510 TWX (1960's/70's), and Canadian TWX Operator from certain provinces (1960's/70's/80's) sometimes from 710/810/910 TWX (1960's/70's),

015 -> 019 - TWX: NPA/510/610 to N10 routings, N10 to 510/610 routings (note that the N10 SAC is converted to 01N)(1960's/70's and Canada 1980's)

020 -> 021 - TWX: N10 (4-R) to NPA (3-R) routings (note 0+NPA) (1960's/70's)

022 -> 029 - (spare- available for: TTC's, pseudo c.o. codes, etc.)

030 -> 031 - TWX: N10 (4-R) to NPA (3-R) routings (note 0+NPA) (1960's/70's)

032 -> 039 - (spare- available for: TTC's, pseudo c.o. codes, etc.)

040 -> 041 - TWX: N10 (4-R) to NPA (3-R) routings (note 0+NPA) (1960's/70's)

042 -> 049 - (spare- available for: TTC's, pseudo c.o. codes, etc.)

050 -> 051 - TWX: N10 (4-R) to NPA (3-R) routings (note 0+NPA) (1960's/70's)

052 -> 059 - (spare- available for: TTC's, pseudo c.o. codes, etc.)

060 -> 061 - TWX: N10 (4-R) to NPA (3-R) routings (note 0+NPA) (1960's/70's)

062 -> 069 - (spare- available for: TTC's, pseudo c.o. codes, etc.)

070 -> 071 - TWX: N10 (4-R) to NPA (3-R) routings (note 0+NPA) (1960's/70's)

072 -> 079 - (RESERVED- for Autovon?)

080 -> 081 - TWX: N10 (4-R) to NPA (3-R) routings (note 0+NPA) (1960's/70's)

082->087,9 - InWATS Tndm routings (third-digit Band; 089 Bnd-1)(1960's/70's)

088 - (spare- available for: TTC's, pseudo c.o. codes, etc.)

090 -> 091 -TWX: N10 (4-R) to NPA (3-R) routings (note 0+NPA) (1960's/70's)

092 -> 099 - (spare- available for: TTC's, pseudo c.o. codes, etc.)

100 - Plant Test: Test Board

101 - Plant Test: Test Board

102 - Plant Test: Milliwatt Tone (~1004 Hz)

103 - Plant Test: Signaling Test Termination

104 - Plant Test: 2-Way Transmission and Noise Test

105 - Plant Test:Auto.Transm.Measurement System/Remote Offc.Test Line

106 - Plant Test: CCSA Loop Transmission Test

107 - Plant Test: Par-Meter Generator

108 - Plant Test: CCSA Loop Echo Support Maintenance

109 - Plant Test: Echo Canceler Test Line

110 -> 119 - Operator Codes

11362 - Air-to-Ground / Maritime-Marine / High-Seas / Trains

115X(1) - Leave Word

116X(1) - Calling-Card Validation System

120 - Network Emergency Center

121 - Inward Operator

122->127,9 - InWATS TSO routings (third-digit Band; 129 Band-1)(1960's/70's)

122 - AT&T Ready-Line 800 (1980's)

128 - (RESERVED)

130 - TWX Assistance Operator (3-Row) (1960's/70's)

131 - Directory Operator

132->137,9 - InWATS TSO routings (third-digit Band; 139 Band-1)(1960's/70's)

138 - Mexico: Hermosillo SON- Numbers routings (pre-1977); IDDD Equal Access routings- 011+ (mid-1980's on)

140 - TWX Assistance Operator (4-Row) (1960's/70's and Canada 1980's)

114 - Rate & Route Operator

142->147,9 - InWATS TSO routings (third-digit Band; 149 Band-1)(1960's/70's)

148 - Mexico: Hermosillo SON- Operators (1970's, 1980's)

150 - Cable Control: Hawaii (WAS 157 until 1977, when PR got 800-468)

151 - International Assistance Operator

152->157,9 - InWATS TSO routings (third-digit Band; 159 Band-1)(1960's/70's)

158 - Mexico: Chihuahua CHI- Numbers routings (pre-1977); IDDD Equal Access routings- 01+ (mid-1980's on)

160 - International Operator Center (IOC)

161 - Trunk Trouble Reporting

162->167,9 - InWATS TSO routings (third-digit Band; 169 Band-1)(1960's/70's)

168 - Mexico: Chihuahua CHI- Operators (1970's, 1980's)

170 - Mexico: Monterrey NL- Numbers routings (pre-1977)

171 - Mexico: Monterrey NL- Operators (1970's, 1980's)

172 - Caribbean: Dom.Rep., Puerto Rico, US Virgin Islands (1970's)

173 - Caribbean: Bahamas (1970's)

174 - Cable Control: Puerto Rico, US Virgin Islands (1970's)

175 - Caribbean: Jamaica (Cayman Islands) (1970's)

176 - Caribbean: Bermuda (1970's); Mexico: Mexicali BCN- Operators (1980's)

177 - Cable Control: Dominican Republic (1970's)

178 - Caribbean: Barbados (Dominica, St.Lucia, St.Vincent) (1970's)

179 - Caribbean: Trinidad/Tobago (Grenada thru 1986) (1970's)

180 - Mexico: Mexico City DF- Numbers routings (pre-1977); Numbers routings for _ALL_ of +52 Mexico (1977-on)

181 - Toll Station Operator (for Ring-Downs)

182 -> 188 - ISCs- International Switching Centers (Gateways):

182 - WHPLNY: 02 0201T 4A (70s); 104T 05 0504T 4E (80s); 103T 03 0203T (90s)

183 - NYCMNY: 04 AA02T 4M (70s); 063T 24 BW24T 4E (80s); 111T 55 BW55T (90s)

184  - PITBPA: 02 DG42T 4A (70s); 076T 03 DG43T 4E (80s); 115T 09 DG09T (90s)

185  - JCVLFL: 02 CL01T 4A (70s); 041T 03 CL03T 4E (80s); ATLNGA: 007T 04 TL01T (90s); VANCBC: 02 0104T 4A (70s)- CANADA

186 - OKLDCA: 03 0341T 4M (70s); 070T 06 0344T 4E (80s); SCRMCA: 083T 04 0404T (90s)

187 - DNVRCA: 03 MA03T 4A (70s); 027T 05 ZJ05T 4E (80s); SHOKCA: 084T 05 0296T (90s)

188 - NYCMNY: 10 BW01T 4A (70s); 062T 50 5450T 4E (80s);?013T -- 5410T (90s)? MTRLPQ: 01 0201T 4A (70s)- CANADA

189 - Mexico: Mexico City DF- Operators (1970's, 1980's)

190 - Mexico: Operator routings for _ALL_ of +52 Mexico (1980's)

191 - Conference Operator Loop-Around (1970's); AT&T Advanced 800 Intercept Recording Frames (1980's)

192 - Cable Control: Jamaica (Cayman Islands) (1970's)

193 - Cable Control: Trinidad/Tobago (Grenada/Carriacou) (1970's)

194 - Cable Control: ?? Bahamas ?? (1970's); Mexico: Tijuana BCN- Operators (1980's)

195 - Cable Control: Antigua/Barbuda (Anguilla, Br. Virgin Islands, Montserrat, St.Kitts/Nevis) (1970's); AT&T Advanced 800 (1980's)

196 - TTC for Oprs/Tst at Wayne PA RC (1960's) as: 196+1X1/11XX/10X  [Wayne was not Principal City for NPA 215 (Philadelphia-2 was), but circa 1972 Wayne got its own 215+0XX+ Oprs/Tst TTC Code]; Cable Control: Barbados (Dominica, St.Lucia, St.Vincent) (1970's); AT&T International 800 (1980's)

197 - Caribbean: Antigua/Barbuda (Anguilla, Br. Virgin Islands, Montserrat, St.Kitts/Nevis) (1970's); AT&T Direct-Services Dialing Concept (1980's)

198 - TTC for Oprs/Tst for Rockdale GA RC (1960's): 198+1X1/11XX/10X [Rockdale was not Principal City for NPA 404 (Atlanta was), but circa 1972 Rockdale got its own 404+0XX+ Oprs/Tst TTC Code]; Cable Control: ?? Bermuda ?? (1970's); AT&T International City Service Center (ICSC) (1980's)

199 -Mexico: Monterrey NL (Oprs? Numbers?) (1960's); Cable Control: Alaska (1970's); AT&T USA Direct (1980's)

11XX(X) - Operator Codes (Leave Word, BLV/Interrupt, Card Validation):

11362 - Mobile / Marine-Maritime / High-Seas / Air-Ground / Trains

1150(1) - Universal or Coin Callback Operator

1151(1) - Conference Operator

1152(1), 1182(1) - Mobile Service / Air-Ground Operator

1153(1), 1183(1) - Marine Service Operator

1154(1), 1188(1) - Toll Terminal Operator

1155(1) - Time and Charges Callback Operator

1156(1) - Hotel / Motel Callback Operator

1157(1) - IOTC Access Trunk

1158(1) - BOC/LEC Inward Completion Assistance

1159(1) - BOC/LEC Inward Busy-Line Verification

1160(1) - Calling Card Validation (Dial-Pulse)

1161(1) - Calling Card Validation (DTMF)

1162(1) - Calling Card Validation (MF)

OLD 3-digit "Step" Service Codes (generic uses; both customer and operator)

112        DDD Toll/Tandem/CAMA Switch Access

113        Directory Assistance (Information)

114        Repair Service

115        Mobile/Marine/Air-Ground/Conference Operator

116        Local Area Toll Station Operator

117        Test Board

118-N-1    Ringback (Multi 4/8/10/Rural Party Lines)

119-1      Ringback (Two-Party Lines)

110        Outward Toll Cordboard Operator